## Slide 1
LESSON LEARN
T40LP CPX4
LAYOUT FOR SIGNAL CELL
BE3 GROUP
Backend Design Dept.
Design Engineering Division
Renesas Design Vietnam Co.,Ltd.
Document number |  | D-IO-T40LP_CPX4-0009-01 | 
Organization |  | BE3/IO | 
Revision No. |  | 1 | 
Approver | Examiner |  | Creator
 | MinhVu Jan.20, 2018 |  | VinhLe Jan.17, 2018

## Slide 2: Agenda
Overview
Power line
Floorplan
Connection
Conclusion and further work

## Slide 3
Overview

## Slide 4: Overview
  Phenomenon/Background
    Layout signal cell is the most difficult in layout IO cells. If we don’t consider properly in the design phase, maybe errors (DRC, EM, …) will occur in verification phase. Some case we must re-design again from beginning. It cause waste resource, shift schedule. It is not good.
    The purpose of this LnL is to discuss about some points we need to consider when layout signal cell
  Scope
    This LnL focus on project T40LP MGA JADE and T40LP CPX4 (40nm).
    It just mention about common points we need to consider and how can we consider them ?

## Slide 5
Power line

## Slide 6: Power line design (1/2)
  We need to consider some points as following:
    Metal structure of power line
    Number of line
    Number of metal for each line
    Width of each metal layer
    Spacing between each metal line
  Purpose: Make sure the power line satisfy the spec (power resistance, DRC rule, EM-ESD, …)
Horizontal power lines
Vertical power lines

## Slide 7: Power line design (2/2)
  How can we consider them?
    Base on spec about cell size, process, position of each power supply, power line resistance, EM-ESD criteria, spacing for PAD terminal, drc rule, PDK we can consider as following:
    PDK => Number of metal for each line
    Power resistance, DRC rule => metal structure of powerline
    Cell height, power line resistance, PAD terminal width, DRC rule => Number of line, width of each metal layer, spacing between each metal line
    Example: Spec: cell height = 185um, cell width = 30, PAD terminal width = 4.5um, power resistance (mohm/um): VDD = 3.3, VSS = 2.5, VCCQ = 1.3, VSSQ = 1.6, PDK 1P7M_4X2Z. Don’t use M7 for power line
    PDK 1P7M_4X2Z => can use M6->M4 for power line, M3->M1 for connection
    Power resistance, DRC rule => metal structure
    Cell height, PAD terminal width => total space for power line  185 – 4.5 = 181.5 um
    Power resistance, cell width, number of metal for each line, DRC rule => 28 VDD lines, 37 VSS lines, 71 VCCQ lines, 58 VSSQ lines (M4 = 0.58um, M5 = 0.56um, M6 = 0.5um for each line)
    EM-ESD criteria and floorplan of ESD device (next part) => number and width of vertical power line
M5
M4
V4
M6
V5
M6
M4
M4
M5
M5
V4
V4
V5
V5
More line
Small resistance
Not need vertical connection
Less line
Large resistance
Need vertical connection
M5
M4
V4
M6
V5
Vertical metal connection

## Slide 8
Floor plan

## Slide 9: Floorplan (1/7)
  We need to consider some points as following:
    Function, type and power supply voltage of each device/block => good power supply, prevent LUP error, easy and make strong connection, EM
    Position of ESD device => better in ESD protection
    Spacing rule for layer which require large space (NW, DNW, …) => enough spacing for wiring
    Clean DRC (spacing, density) for lower layer => make sure the floorplan is fixed
  Purpose: Make sure the floorplan is fixed, achievable, reduce error in verification phase as much as possible

## Slide 10: Floorplan (2/7)
  Function, type and power supply voltage of each device/block
  Position of ESD device
  How can we consider them ?
    Level shifter part:
    Function: change voltage level of signal from core domain to IO domain and vice verse
    Have pin connect direct to core domain
    Power supply: core (low) and IO (high)
    => Suggestion floorplan
      + Place in the top cell: easy for connecting to core side
      + Near core voltage power: better power supply
      + Separate P-type and N-type
ESD devices
Level shifter part
Internal logic part
Output buffer part
PAD
Project: T40LP MGA JADE
Lib name: TC40APA25G_4X2Z
Cell name: PA25GC33BA0EWAZ

## Slide 11: Floorplan (3/7)
  How can we consider them ?
    Internal logic part:
    Function: Control to transfer signal from core domain to IO domain and vice versa
    Power supply: IO voltage (VCCQ)
    => Suggestion floorplan
      + Place in middle of cell (below level shifter): easy for connecting to level shifter output buffer and ESD devices
      + Put near IO voltage power: better power supply
      + Separate P-type and N-type
ESD devices
Level shifter part
Internal logic part
Output buffer part
PAD
Project: T40LP MGA JADE
Lib name: TC40APA25G_4X2Z
Cell name: PA25GC33BA0EWAZ

## Slide 12: Floorplan (4/7)
  How can we consider them ?
    Output buffer part:
    Function: Main buffer for output path (I -> PAD) in signal cell.
    Power supply: IO voltage (VCCQ)
    Connect directly to PAD (need to consider latch-up)
    => Suggestion floorplan:
      + Place in bottom of cell:
        - Make the distance between level shifter part (core voltage) and buffer part (IO voltage) largest to prevent LUP error
      + Put near IO voltage power: better power supply
      + Distance between PMOS and NMOS as large as possible: prevent LUP error
ESD devices
Level shifter part
Internal logic part
Output buffer part
PAD
Project: T40LP MGA JADE
Lib name: TC40APA25G_4X2Z
Cell name: PA25GC33BA0EWAZ

## Slide 13: Floorplan (5/7)
  How can we consider them ?
    ESD devices:
    Function: ESD protection
      + Resistance: prevent ESD current (from PAD) flow into output buffer and logic circuit
      + Diode: dis-charge ESD current (from PAD)
    Power supply: IO voltage (VCCQ)
    Connect directly to PAD (need to consider latch-up)
    => Suggestion floorplan:
      + Should place so that the ESD current must flow through ESD devices before flow into devices be protected
      + Diode => Place between PMOS and NMOS of output buffer: Make the distance between PMOS and NMOS larger
ESD devices
Level shifter part
Internal logic part
Output buffer part
PAD
Project: T40LP MGA JADE
Lib name: TC40APA25G_4X2Z
Cell name: PA25GC33BA0EWAZ

## Slide 14: Floorplan (6/7)
  Combine all of above factor we have following floorplan (T40LP MGA JADE):
Level shifter part
Internal logic part
Output buffer (NMOS)
Output buffer (PMOS)
ESD devices
(Diode)
Resistor
PAD
Resistor
VDD
VSS
VCCQ
VSSQ
VSSQ
VCCQ
ESD devices
Level shifter part
Internal logic part
Output buffer part
PAD
Project: T40LP MGA JADE
Lib name: TC40APA25G_4X2Z
Cell name: PA25GC33BA0EWAZ

## Slide 15: Floorplan (7/7)
    Spacing rule for layer which require large space (NW, DNW, …)
    Clean DRC (spacing, density) for lower layer
NW, DNW rules
(Document No. : TN45CLDR001_2_4
Version: 2.4)
  How can we consider them?
    Check devices structure => to know the layers of each device
    Check design manual => to know the spacing rule, density rule
    Run DRC => to make sure all lower layer have clean DRC

## Slide 16
Connection

## Slide 17: Connection (1/4)
  We need to consider some points as following:
    EM-ESD calculation
    ESD net and high voltage net must be as large as possible
  Purpose: Better in prevent ESD, improve current driving ability, reduce EM-SIGRA violation as much as possible

## Slide 18: Connection (2/4)
Connection from PAD to ESD devices
Output buffer connection
PAD
Project: T40LP MGA JADE
Lib name: TC40APA25G_4X2Z
Cell name: PA25GC33BA0EWAZ
POWER
GND
Logic connection
  How can we consider them ?
    Connection from PAD to ESD devices:
    Function:
      + Normal operation: transfer signal
      + ESD occur: flow ESD current from PAD to ESD devices
    => Suggestion connection:
      + Width: as large as possible
      + Via, contact: as much as possible
      + Resistance: as small as possible
      + EM-ESD: should have margin compare with Spec

## Slide 19: Connection (3/4)
  How can we consider them ?
    Output buffer connection
    Function:
      + Normal operation: current buffer
      + ESD occur: flow ESD current (smaller than ESD net due to have resistor in front of buffer)
    => Suggestion connection:
      + Width: as large as possible
      + Resistance: as small as possible
      + Via, contact: as much as possible
      + EM-ESD: should have margin compare with Spec
Net connected to ESD devices
PAD
Project: T40LP MGA JADE
Lib name: TC40APA25G_4X2Z
Cell name: PA25GC33BA0EWAZ
Logic connection
Output buffer connection
POWER
GND
GND connection
DRAIN connection
Output buffer/NMOS
GND Diode

## Slide 20: Connection (4/4)
Connection from PAD to ESD devices
Output buffer connection
PAD
Project: T40LP MGA JADE
Lib name: TC40APA25G_4X2Z
Cell name: PA25GC33BA0EWAZ
POWER
GND
Logic connection
  How can we consider them ?
    Logic connection
    Function: logic control and transfer signal
    => Suggestion connection:
      + Width: based on voltage of each net. High voltage net need large width
      + Via, contact: as much as possible
      + Uniform in wiring (Ex: odd metal is vertical, even is horizontal)

## Slide 21
Conclusion and further work

## Slide 22: Conclusion (1/2)
  This LnL just show common point we need to consider while layout signal cells. It is not total properly for all project. Some project, we can get good result for this part but the other is not so good and vice versa. In that case, we must trade off between them based on the priority and spec. If there is issue occur due to trade off, we must find the countermeasure to solve the issue.
  Example about trade off in project T40LP CPX4 (next page)
 | Considering points | Suggestion
Power line | Metal structure Number of line, number of metal per line Width and spacing | PDK => Number of metal for each line Power resistance, DRC rule => metal structure of powerline Cell height, power line resistance, PAD terminal width, DRC rule => Number of line, width of each metal layer, spacing between each metal line
Floorplan | Level shifter part Internal logic part Output buffer part ESD devices | Place in the top cell; Put near core voltage power; Separate P-type and N-type Place in middle of cell (below level shifter); Put near IO voltage power; Separate P-type and N-type Place in bottom of cell; Make the distance between level shifter part (core voltage) and buffer part (IO voltage) largest; Put near IO voltage power; Distance between PMOS and NMOS as large as possible Should place so that the ESD current must flow through ESD devices before flow into devices be protected; Place diode between PMOS and NMOS of output buffer
Connection | from PAD to ESD devices; Output buffer connection Logic connection | Width: as large as possible; Via, contact: as much as possible; Resistance: as small as possible; EM-ESD: should have margin compare with Spec Width: based on voltage of each net. High voltage net need large width; Via, contact: as much as possible; Uniform in wiring (Ex: odd metal is vertical, even is horizontal)

## Slide 23: Conclusion (2/2)
  In this project, spec of cell height is 80um => do not have enough space to floorplan as above recommendation => must trade off to meet spec (80 um)
    ESD devices + Output buffer + driver control: left side
    Level shifter: right side (top)
    Internal logic: right side (bottom)
  Issue: ESD devices and output buffer near level shifter => Latch-up occur
  Countermeasure => using double guard-ring and investigate LUP rules in design manual to have a properly spacing
Driver control
Output buffer/ PMOS
Output buffer/ NMOS
PMOS diode
NMOS diode
Level shifter part
Internal logic part

## Slide 24: Further work
  This LnL just show common point we need to consider while layout signal cells. There are some point we need to make more detail in the future (by LnL or sharing document):
    Power line resistance calculation
    Latch-up prevention => What? When? Where? Why? How to prevent ?

## Slide 25
Renesas System Design Co., Ltd.